GREEN SAFE SYSTEM_INTENSIVE HANGING GREENERY_70/30 – LAWN AND SHRUBS
The GreenSafe Lawn and Shrubs hanging system has a thickness of 20 cm/ 7,87 inchs for the lawn areas, which represent the 70% of the total surface, and a thickness of 25 cm/ 9,84 inchs for the remaining 30%. The weight at maximum saturation level is up to 290 kg/sqm 639 lb/sqm, net of Flora.

SPECIFICATION ITEMS
0.	LAYING SURFACE
	The waterproofing system has to be leak-proof tested and roots-proof certified. / Surfaces have to be clear and clean, without any sharp edge or area, with regular gradients ( > 1%).
1.	ELEMENT OF WATER STORAGE, AERATION, DRAINAGE AND FILTERING
	Modular element STORE MOD, thickness 5 cm (1,96 inches), consist of: retread non-toxic polyester felt 800 gr/sqm weight, size 600/800 mm, with mechanic protection, horizontal and vertical draining function; expanded perlite filling, size 0.1-0.2 mm, with ventilation and store&drain water function; geotextile high toughness polypropylene staple nonwoven cover element,130gr/square meter weight, with filtration and division function from the grown substrate. / Technical Features: / -Thickness: 5 cm; / -Size: 60 x 80 cm; / -pH: 6-7; / -Dry weight: 7 Kg/mq; / -Weight at maximum saturation: 35,00 Kg/m2; / -Water storage capacity: 32 l/m2; / -Storage element porosity: 95%; / -Air Volume at pF1: > 30%; / -Water Volume at pF1: >60%; / -Thermal conductivity lambda: 0.050 W/mk dry; 0.222 W/mk saturation at 100 % / All the elements got CE mark where is needed and comply with UNI11235 law. / GEO GAP and FILTRASAFE supply quantity according to levelling areas (perimeter and emerging parts).
2.	INTENSIVE GREENING SUBSTRATE
	SB Intensive light Substrate: intensive greening substrate consist of an appropiate blend of peat, lapillum, pumice and zeolite laid by a 15 cm/5,9 inch (compation index included) overall thickness or according agronomic needs of species planted. / Technical features: / -compacted thickness 15 cm (compaction index 16%) -70% of the total surface / compacted thickness 20 cm (compaction index 16%) -30% of the total surface / -Size: 0-16 mm; / -Dry apparent volume density: 634 ± 5% kg/m3; / -Weight at potential saturation: 1095 Kg/m3; (*) / - Total porosity v/v: >60%; / -Air volume at pF1: > 18% v/v; / - Water volume at pF1. > 30% v/v; / -pH: 4-8,5; / -Electric conductivity: ≤ 60 mS/m; / -Cation exchange capacity: > 20 meq/100g s.s; / -Organic matter: < 80 g/l s.s.; / -phytotoxicity eligible0; / -Volume reduction grade under compressive strees: ≤ 16 % / The product comply with UNI 11235:15 law requirements / (*) Maximum saturation at pF 0,7 (UNI EN 13041:2012), Water volume at pF 0,7 > 40 %.
3.	VEGETATION
	Lawn
	Greening by pregrown turfgrass rolls installation, consists of Festuca arundinacea (90%) and Poa prantensis (10%) blend of seeds).
	Greening by the direct sown of a seeds blend according the characteristic and the adhibition of the project area.
	Shrubs
	Greening by shrubs in different species installation, 18 cm pots size, in the range of 3 plants/sqm selected according surrondings area.
4.	IRRIGATION SYSTEM
	Irrigation system consisting in sub-irrigation dripping system to the lawn greening surface (70% of the total) and on drip-pipe irrigation system to the schrubs greening area (30% of the total). Control unit, bistable solenoid valves, sprinklers and dripping pipe/sub-irrigation pipe (according projects precepts) are included.
5.	HANGING SYSTEMS ACCESSORIES
	Inspection drainage concrete sumps, color grey, size 20x20cm, including h 5 cm traps and draining extension in order to achieve hanging package project height.