GREEN SAFE SYSTEM_INTENSIVE HANGING SYSTEM
General Features of the system: The average thickness of the system is 40cm (15.74 inchs). It consists of the STORE MOD (Element which guarantees proper storage, drainage and filtering of the water. Thickness 5 cm/1.96 inchs), the technical GS INTENSIVE SUBSTRATE (Thickness 25cm/9.87 inchs, including compaction index) and the GS GeoGap 5-10 LAPILLI which work as a thickness compensation (Thickness 10 cm/3.93 inchs, including compaction index). The weight at maximum saturation level is up to 425 Kg/sqm (937 lb/sqm). Net of Flora.

SPECIFICATION ITEMS
0.	LAYING SURFACE
	The waterproofing system has to be leak-proof tested and roots-proof certified. / Surfaces have to be clear and clean, without any sharp edge or area, with regular gradients ( > 1%).
1.	ELEMENT OF WATER STORAGE, AERATION, DRAINAGE AND FILTERING
	Modular element STORE MOD, thickness 5 cm (1,96 inches), consist of: retread non-toxic polyester felt 800 gr/sqm weight, size 600/800 mm, with mechanic protection, horizontal and vertical draining function; expanded perlite filling, size 0.1-0.2 mm, with ventilation and store&drain water function; geotextile high toughness polypropylene staple nonwoven cover element,130gr/square meter weight, with filtration and division function from the grown substrate. / Technical Features: / -Thickness: 5 cm; / -Size: 60 x 80 cm; / -pH: 6-7; / -Dry weight: 7 Kg/mq; / -Weight at maximum saturation: 35,00 Kg/m2; / -Water storage capacity: 32 l/m2; / -Storage element porosity: 95%; / -Air Volume at pF1: > 30%; / -Water Volume at pF1: >60%; / -Thermal conductivity lambda: 0.050 W/mk dry; 0.222 W/mk saturation at 100 % / All the elements got CE mark where is needed and comply with UNI11235 law. / GEO GAP and FILTRASAFE supply quantity according to levelling areas (perimeter and emerging parts).
2.	INTENSIVE GREENING SUBSTRATE
	SB Intensive light Substrate: intensive greening substrate consist of an appropiate blend of peat, lapillum, pumice and zeolite laid by a 25cm/9.87 inch (compation index included) overall thickness or according agronomic needs of species planted. / Technical features: / -compacted thickness 25 cm (compaction index 16%) / -Size: 0-16 mm; / -Dry apparent volume density: 634 ± 5% kg/m3; / -Weight at potential saturation: 1095 Kg/m3; (*) / - Total porosity v/v: >60%; / -Air volume at pF1: > 18% v/v; / - Water volume at pF1. > 30% v/v; / -pH: 4-8,5; / -Electric conductivity: ≤ 60 mS/m; / -Cation exchange capacity: > 20 meq/100g s.s; / -Organic matter: < 80 g/l s.s.; / -phytotoxicity eligible; / -Volume reduction grade under compressive strees: ≤ 16 % / The product comply with UNI 11235:15 law requirements / (*) Maximum saturation at pF 0,7 (UNI EN 13041:2012), Water volume at pF 0,7 > 40 %.
3.	VEGETATION
	Lawn
	Greening by pregrown turfgrass rolls installation.
	Shurbs
	Greening by shrubs in different species installation, 18 cm pots size, in the range of 3 plants/sqm selected according surrondings area.
	Trees
	Small trees, 10/12 cm (4-5 inchs) circumference stem, selected according surrondings area.
4.	IRRIGATION SYSTEM
	Sprinkler Irrigation system to the lawn area (70%), dripping pipe to the schrubs (20%) and the trees area (10%). The system includes the control units, the bistable solenoid valve, sprinklers and dripline pipe.
5.	HANGING SYSTEMS ACCESSORIES
	Inspection drainage concrete sumps, color grey, size 20x20cm, including h 5 cm traps and draining extension in order to achieve hanging package project height.