GREEN SAFE SYSTEM_INTENSIVE HANGING GREENERY – SLOPE
The GreenSafe slope intensive hanging system, greening by lawn, has an overall standard thickness of 20cm/13.77inchs and a weight at maximum saturation level up to 225kg/sqm - 496lb/sqm, net of flora. / The implementation of this stratigraphy needs the inclusion of appropiate restraint elements which allowed the laying on surface up to 45 degrees rake angle.

	SPECIFICATION ITEMS
0.	LAYING SURFACE
	Il sistema impermeabile dovrà essere collaudato a tenuta idraulica e certificato antiradice.
1.	ELEMENT OF STABILISATION AND STRENGTHENING: GS GRIPMOD
	Bidimensional full junture Geogrid, made of 100% heavy duty polyethilene with high mechanical and tensional resistance, designed to provide restraint and stability to the slope hanging system all.
2.	ELEMENT OF ANCHORING: GS PIPE MOD
	Anchoring element made of polyethilene hard pipes, diameter 32m, fixed to the stabilizer element, in order to restraint the stratigraphy by the use of high density heavy duty polyethilene zip ties, which are heavy load and wear-proof.
3.	ELEMENT OF WATER STORAGE, AERATION, DRAINAGE AND FILTERING
	Extensive light greening substrate consist of peat, lapillum, pumice and zeolite laid by an 8 cm/ 3,1 inch (compaction index included) overall thickness or according agronomic needs of species planted. / Technical features: / Compaction index : 16% / -Size: 0-10 mm; / -Dry apparent volume density: 697 ± 5% kg/m3; / -Weight at potential saturation: 1144 Kg/m3; (*) / -Total porosity v/v: >60%; / -Air volume at pF1: > 15%; / -Water volume at pF1 : > 30%; / -pH: 7-8; / -Electric conductivity: < 50 mS/m; / -Cation exchange capacity > 20 meq/100g s.s; / -Organic Matter: < 60 g/l s.s; / -phytotoxicity eligible; / -Volume reduction grade under compressive strees: ≤16 % / The product comply with UNI 11235:15 law requirements / (*) Maximum saturation at pF 0,7 (UNI EN 13041:2012), Water volume at pF 0,7 > 40 %.
4.	ELEMENT OF RESTRAINT AND EROSION-PREVENT: GS TERRAGRIP
	Restraint element consists of panels made by high density polyethylene cells, 75 mm thickness, which form a restraint 3D alveolar structure to confine the cultivation substrate.
5.	INTENSIVE GREENING SUBSTRATE
	SB Intensive light Substrate: intensive greening substrate consist of an appropiate blend of peat, lapillum, pumice and zeolite laid by a 15 cm/5,9 inch (compation index included) overall thickness or according agronomic needs of species planted. / Technical features: / -compacted thickness 15 cm (compaction index 16%) / -Size: 0-16 mm; / -Dry apparent volume density: 634 ± 5% kg/m3; / -Weight at potential saturation: 1095 Kg/m3; (*) / - Total porosity v/v: >60%; / -Air volume at pF1: > 18% v/v; / - Water volume at pF1. > 30% v/v; / -pH: 4-8,5; / -Electric conductivity: ≤ 60 mS/m; / -Cation exchange capacity: > 20 meq/100g s.s; / -Organic matter: < 80 g/l s.s.; / -phytotoxicity eligible0; / -Volume reduction grade under compressive strees: ≤ 16 % / The product comply with UNI 11235:15 law requirements / (*) Maximum saturation at pF 0,7 (UNI EN 13041:2012), Water volume at pF 0,7 > 40 %.
6.	VEGETATION
	Greening by pregrown turfgrass rolls installation, consists of blend of seeds of Festuca arundinacea (90%) and Poa prantensis (10%).
7.	IRRIGATION SYSTEM
	Sub-irrigation system consist of a pre-drilled anti-roots 16mm diametr pipe, divided into appropiate areas controlled by 1” 9V bistable solenoid valves and 9V battery control unit, including everything necessary to guarantee the hand-over and acceptance test. (excluding water supply predisposition, which is up to the client).